| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLFLEX District cooling system DN 20 – 125 (ø 25 – 125 mm) Suitable up to max. -20°C / +40°C* and 16 bar, longitudinally watertight, comprising: medium pipe in PE100, insulation made of continuously manufactured CFC-free, CO2-blown flexible rigid polyurethane foam (l-Value ≤ 0.0234 W/mK), PE foil and a sinusoidally corrugated, seamlessly extruded-on polyethylene (LLD-PE) outer casing, including factory test. Delivered on drums or in rings COOLFLEX District cooling system cont. m COOLFLEX 25/76 3/4“ DN 20 cont. m COOLFLEX 32/76 1“ DN 25 cont. m COOLFLEX 40/91 1 1/4“ DN 32 cont. m COOLFLEX 50/91 1 1/2" DN 40 cont. m COOLFLEX 63/126 2“ DN 50 cont. m COOLFLEX 75/126 2 1/2“ DN 65 cont. m COOLFLEX 90/162 3“ DN 80 cont. m COOLFLEX 110/162 4“ DN 100 cont. m COOLFLEX 125/182 5“ DN 125 further dimensions on request *warm water application with limited lifetime and operating pressure (as per DIN 8074) |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | COOLFLEX house lead-in bend, 90° Leg length 1.1 x 1.6m. longitudinally watertight, medium pipe in PE-HD, insulation made of CFC-free CO2-blown rigid polyurethane foam, protective casing in polyethylene (PE-HD). COOLFLEX bend 90° Unit: COOLFLEX 25/76 3/4“ DN 20 Unit: COOLFLEX 32/76 1“ DN 25 Unit: COOLFLEX 40/91 1 1/4“ DN 32 Unit: COOLFLEX 50/91 1 1/2“ DN 40 Unit: COOLFLEX 63/126 2“ DN 50 Unit: COOLFLEX 75/126 2 1/2“ DN 65 Unit: COOLFLEX 90/162 3“ DN 80 Unit: COOLFLEX 110/162 4“ DN 100 Unit: COOLFLEX 125/182 5“ DN 125 |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | COOLFLEX sealing ring consisting of a specially profiled neoprene ring, suitable for: outer diameter of COOLFLEX 76 mm outer diameter of COOLFLEX 91 mm outer diameter of COOLFLEX 111 mm outer diameter of COOLFLEX 126 mm outer diameter of COOLFLEX 142 mm outer diameter of COOLFLEX 162 mm outer diameter of COOLFLEX 182 mm Sealing ring for wall leadthrough, impermeable to water pressure < 0.5 bar, seal insert type A (centering) and type C40 (sealing) for core bore or pipe liner, suitable for: outer diameter of COOLFLEX 76 mm outer diameter of COOLFLEX 91 mm outer diameter of COOLFLEX 111 mm outer diameter of COOLFLEX 126 mm outer diameter of COOLFLEX 142 mm outer diameter of COOLFLEX 162 mm outer diameter of COOLFLEX 182 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLFLEX shrink-on end cap for damp zones Heat-shrink closure for house lead-ins, consisting of: molecular cross-linked and modified polyolefin, coated with sealing adhesive with temperature resistance up to 125°C. Including temperature measuring strip and abrasive strip. or End cap for COOLFLEX for dry zones suitable for: Unit: COOLFLEX 25/76 3/4“ DN 20 Unit: COOLFLEX 32/76 1“ DN 25 Unit: COOLFLEX 40/91 1 1/4“ DN 32 Unit: COOLFLEX 50/91 1 1/2“ DN 40 Unit: COOLFLEX 63/126 2“ DN 50 Unit: COOLFLEX 75/126 2 1/2“ DN 65 Unit: COOLFLEX 90/162 3“ DN 80 Unit: COOLFLEX 110/162 4“ DN 100 Unit: COOLFLEX 125/182 5“ DN 125 |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLFLEX connecting piece, screwed connection to connect with onward pipes PE connecting piece in brass with external thread, suitable for: PE pipe DN External thread 25 x 2.3 mm 20 3/4“ 32 x 2.9 mm 25 1“ 40 x 3.7 mm 32 1 1/4“ 50 x 4.6 mm 40 1 1/2“ 63 x 5.8 mm 50 2“ 75 x 6.8 mm 65 2 1/2“ 90 x 8.2 mm 80 3“ 110 x 10 mm 100 4“ COOLFLEX coupling, screwed connection, equal in brass, to connect two COOLFLEX pipes (without insulation material), suitable for: PE pipe DN PE pipe DN 25 x 2.3 mm 20 25 x 2.3 mm 20 32 x 2.9 mm 25 32 x 2.9 mm 25 40 x 3.7 mm 32 40 x 3.7 mm 32 50 x 4.6 mm 40 50 x 4.6 mm 40 63 x 5.8 mm 50 63 x 5.8 mm 50 75 x 6.8 mm 65 75 x 6.8 mm 65 90 x 8.2 mm 80 90 x 8.2 mm 80 110 x 10 mm 100 110 x 10 mm 100 COOLFLEX coupling, screwed connection, reduced, in brass, to connect two COOLFLEX pipes (without insulation material), suitable for: PE pipe DN PE pipe DN 32 x 2.9 mm 25 25 x 2.3 mm 20 40 x 3.7 mm 32 32 x 2.9 mm 25 50 x 4.6 mm 40 40 x 3.7 mm 32 |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | COOLFLEX coupling, screwed connection Condinuance 63 x 5.8 mm 50 50 x 4.6 mm 40 75 x 6.8 mm 65 63 x 5.8 mm 50 90 x 8.2 mm 80 75 x 6.8 mm 65 65 75 x 6.8 mm 65 110 x 10 mm 100 90 x 8.2 mm 80 90 x 8.2 mm 80 COOLFLEX coupling 90°, screwed connection, equal in brass, to connect two COOLFLEX pipes (without insulation material), suitable for: PE pipe DN 32 x 2.9 mm 25 40 x 3.7 mm 32 50 x 4.6 mm 40 63 x 5.8 mm 50 75 x 6.8 mm 65 90 x 8.2 mm 80 110 x 10 mm 100 COOLFLEX - T-piece, screwed connection for PE pipes (without insulating material) up to multiple-stage reduction, suitable for: Unit: 25-25-25 mm Unit: 32-32-32 mm Unit: 32-25-32 mm Unit: 32-25-25 mm Unit: 40-40-40 mm Unit: 40-32-40 mm Unit: 40-25-40 mm Unit: 40-32-32 mm Unit: 40-25-32 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLFLEX - T-piece, screwed connection Condinuance Unit: 50-50-50 mm Unit: 50-40-50 mm Unit: 50-32-50 mm Unit: 50-25-50 mm Unit: 50-40-40 mm Unit: 50-32-40 mm Unit: 50-25-40 mm Unit: 63-63-63 mm Unit: 63-50-63 mm Unit: 63-40-63 mm Unit: 63-32-63 mm Unit: 63-25-63 mm Unit: 63-50-50 mm Unit: 63-40-50 mm Unit: 63-32-50 mm Unit: 63-25-50 mm Unit: 75-75-75 mm Unit: 75-63-75 mm Unit: 75-50-75 mm Unit: 75-40-75 mm Unit: 75-32-75 mm Unit: 75-25-75 mm Unit: 75-63-63 mm Unit: 75-50-63 mm Unit: 75-40-63 mm Unit: 75-32-63 mm Unit: 75-25-63 mm Unit: 90-90-90 mm Unit: 90-75-90 mm Unit: 90-63-90 mm Unit: 90-50-90 mm Unit: 90-40-90 mm Unit: 90-32-90 mm Unit: 90-25-90 mm Unit: 90-75-75 mm Unit: 90-63-75 mm Unit: 90-50-75 mm Unit: 90-40-75 mm Unit: 90-32-75 mm Unit: 90-25-75 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLFLEX - T-piece, screwed connection Condinuance Unit: 110-110-110 mm Unit: 110-90-110 mm Unit: 110-75-110 mm Unit: 110-63-110 mm Unit: 110-50-110 mm Unit: 110-40-110 mm Unit: 110-32-110 mm Unit: 110-25-110 mm Unit: 110-90-90 mm Unit: 110-75-90 mm Unit: 110-63-90 mm Unit: 110-50-90 mm Unit: 110-40-90 mm Unit: 110-32-90 mm Unit: 110-25-90 mm COOLFLEX -T-shell (ø 76 mm - 126 mm) T-piece set with ABS half shells comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (16 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe 76-76-76 mm Unit: outer pipe 91-91-91 mm Unit: outer pipe 91-76-91 mm Unit: outer pipe 91-76-76 mm Unit: outer pipe 111-111-111 mm Unit: outer pipe 111-91-111 mm Unit: outer pipe 111-76-111 mm Unit: outer pipe 111-76-91 mm Unit: outer pipe 111-76-76 mm Unit: outer pipe 111-91-91 mm Unit: outer pipe 111-76-91 mm Unit: outer pipe 111-76-76 mm COOLFLEX -T-shell Condinuance Unit: outer pipe 126-126-126 mm Unit: outer pipe 126-111-126 mm Unit: outer pipe 126-91-126 mm Unit: outer pipe 126-76-126 mm Unit: outer pipe 126-111-111 mm Unit: outer pipe 126-91-111 mm Unit: outer pipe 126-76-111 mm Unit: outer pipe 126-91-91 mm Unit: outer pipe 126-91-76 mm Unit: outer pipe 126-76-91 mm Unit: outer pipe 126-76-76 mm COOLFLEX -T-piece are freely reducible from ø 76 mm – 126 mm COOLFLEX -Big-T-shell (ø 142 mm – 182 mm) T-piece set with ABS half shells comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (27 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe 142-142-142 mm Unit: outer pipe 142-126-142 mm Unit: outer pipe 142-111-142 mm Unit: outer pipe 142-91-142 mm Unit: outer pipe 142-76-142 mm Unit: outer pipe 142-126-126 mm Unit: outer pipe 142-111-126 mm Unit: outer pipe 142-91-126 mm Unit: outer pipe 142-76-126 mm Unit: outer pipe 162-162-162 mm Unit: outer pipe 162-142-162 mm Unit: outer pipe 162-126-162 mm Unit: outer pipe 162-111-162 mm Unit: outer pipe 162-91-162 mm Unit: outer pipe 162-76-162 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | COOLFLEX -Big-T-shell Condinuance Unit: outer pipe 162-142-142 mm Unit: outer pipe 162-126-142 mm Unit: outer pipe 162-111-142 mm Unit: outer pipe 162-91-142 mm Unit: outer pipe 162-76-142 mm Unit: outer pipe 182-182-182 mm Unit: outer pipe 182-162-182 mm Unit: outer pipe 182-142-182 mm Unit: outer pipe 182-126-182 mm Unit: outer pipe 182-111-182 mm Unit: outer pipe 182-91-182 mm Unit: outer pipe 182-182-162 mm Unit: outer pipe 182-162-162 mm Unit: outer pipe 182-142-162 mm Unit: outer pipe 182-126-162 mm Unit: outer pipe 182-111-162 mm Unit: outer pipe 182-91-162 mm Unit: outer pipe 182-182-142 mm Unit: outer pipe 182-162-142 mm Unit: outer pipe 182-142-142 mm Unit: outer pipe 182-126-142 mm Unit: outer pipe 182-111-142 mm Unit: outer pipe 182-91-142 mm COOLFLEX -T-piece are freely reducible from ø 76 mm – 182 mm COOLFLEX -I-shell (ø 76 mm - 126 mm) T-piece set with ABS half shells comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (12 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe 76-76 mm Unit: outer pipe 91-91 mm Unit: outer pipe 91-76 mm Unit: outer pipe 111-111 mm Unit: outer pipe 111-91 mm Unit: outer pipe 126-126 mm Unit: outer pipe 126-111 mm COOLFLEX -I-pieces are freely reducible from ø 76 mm – 126 mm COOLFLEX -Big-I-shell (ø 142 mm – 182 mm) I-piece set with ABS half shells comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (22 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe 142-142 mm Unit: outer pipe 142-126 mm Unit: outer pipe 162-162 mm Unit: outer pipe 162-142 mm Unit: outer pipe 182-182 mm Unit: outer pipe 182-162 mm COOLFLEX –Big-I-pieces are freely reducible from ø 76 mm – 182 mm COOLFLEX -L-shell (ø 76 mm - 126 mm) T-piece set with ABS half shells comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (14 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe 76-76 mm Unit: outer pipe 91-91 mm Unit: outer pipe 111-111 mm Unit: outer pipe 126-126 mm Die COOLFLEX -Schalen sind frei reduzierbar von ø 76 mm – 126 mm COOLFLEX -Big-L-shell (ø 142 mm – 182 mm) L-piece set with ABS half shells comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (24 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe 142-142 mm Unit: outer pipe 162-162 mm Unit: outer pipe 182-182 mm COOLFLEX –Big-L-pieces are freely reducible from ø 76 mm – 182 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | COOLFLEX joint set Type COOLFLEX - COOLFLEX for 16 bar pipes, with insulating material: foam packing in polyurethane foam or PE foam, comprising: one PEH joint pipe (for reduction joints: reduced on one side), two PE shrink-on sleeves, foam packing in polyurethane foam or PE foam, and one abrasive strip. Joint set, COOLFLEX - COOLFLEX for COOLFLEX with PUR foam packing, to match the outer diameter: Unit: 76 mm to 76 mm Unit: 91 mm to 91 mm Unit: 91 mm to 76 mm Unit: 111 mm to 111 mm Unit: 111 mm to 91 mm Unit: 126 mm to 126 mm Unit: 126 mm to 111 mm Unit: 142 mm to 142 mm Unit: 142 mm to 126 mm Unit: 162 mm to 162 mm Unit: 162 mm to 142 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | Joint set, COOLFLEX - COOLFLEX for COOLFLEX with PE foam, to match outer pipe diameters: Unit: 76 mm to 76 mm Unit: 91 mm to 91 mm Unit: 91 mm to 76 mm Unit: 111 mm to 111 mm Unit: 111 mm to 91 mm Unit: 126 mm to 126 mm Unit: 126 mm to 111 mm Unit: 142 mm to 142 mm Unit: 142 mm to 126 mm Unit: 162 mm to 162 mm Unit: 162 mm to 142 mm |  |  |